Need coverage and rate equations

ital{%theta_{AS} = {alignc %kappa_{ ads } %psi} over {1 + %kappa_{ ads } %psi}} " = coverage of surface by adsorbed A"

"rate" = ital{ %phi^2{alignc %psi} over {(1 + %kappa_{ ads } %psi)^2}} ; at steady state , ital{ {d^2 %psi} over {d %lambda^2} = %phi^2{alignc %psi} over {(1 + %kappa_{ ads } %psi)^2}}

Need coverage and rate equations

ital{%theta_{AS} = {alignc %kappa_{ ads } %psi} over {1 + %kappa_{ ads } %psi}} " = local coverage of surface by adsorbed A ; local reaction rate " = ital{ {alignc %kappa_{ rxn } %kappa_{ ads } %psi} over {(1 + %kappa_{ ads } %psi)^2}}"

"local reaction rate " = ital{ %phi^2{alignc %psi} over {(1 + %kappa_{ ads } %psi)^2}}

left ( {V_cell} over {V_layer} right ){d %psi_c} over {d %tau} = %kappa_flow (%psi_{"in"} - %psi_c) - %kappa_diff left [ {d %psi} over {d %lambda} right ]_{%lambda = 1} "where " %psi_c = " reactant in mixing cell"

Need Kflow

%kappa_flow = {alignc Q} over {V_{layer} k_{-1}} = {alignc Q} over {V_{cell} k_{-1}} left ( {V_cell} over {V_layer} right ) " where " Q ("m"^3" s"^-1) " = flow rate through mixing cell"

Reaction rate as dimensionless turnover frequency (TOF):

"d'less TOF" = {alignc "mol A reacting"} over {"(mol surface sites)" "(dimensionless time)"} newline phantom "d'less TOF" = {alignc -r_A ("mol"_{A,gas,layer} " m"_layer^-3 " s"^-1 )} over { %alpha ("mol"_{surf,layer}^{max} " mol"_{A,gas,layer}^{max,-1}) %epsilon ("m"_void^3 "m"_layer^-3) C_{A,gas}^max ("mol"_{A,gas,layer}^max " m"_void^-3) k_-1( "s"^-1 )}